## Slide 1
RE510 SLAM
Occupancy grid map & MCL
What to do?

## Slide 2: TASK 1 : Occupancy Gridmap
It’s simple. Make occupancy gridmap!
Refer to video mapgen.mp4
You have to make the image like gridmap.png
  Do not have to save image. Just show me the video is enough.
You have to edit the source code
  re510_slam/rs_mapgen/src/mapgen.cpp
You have to use the rosbag file
  지도제작.bag
You can run the program by..
  rosrun re510_slam rs_mapgen
  rosbag play dir_of_지도제작.bag

## Slide 3: TASK 2 : MCL(particle filter)
Predict where the robot is!
Refer to video mcl.mp4
Do not have to evaluate. Just show me the video is enough.
You have to edit the source code
  re510_slam/rs_mcl/src/mcl.cpp
You have to use the rosbag file
  위치인식.bag
You can run the program by..
  rosrun re510_slam rs_mcl
  rosbag play dir_of_위치인식.bag

## Slide 4: Readme
gridmap.png is generated map using completed mapgen code.
erodedGridmap.png is modified from gridmap.png for MCL.
In tool folder, there are some useful tools.
  Maybe you don’t have to use in this lab, but you can use it your project!
For MCL, because the environment is too square and the sensor is not good and the results may be bad.
  Just show me the prediction – correction – resampling works well.

## Slide 5: Submit
Due : 4/14(Sun) 23:59.
Late submission will get lower score.
E-mail : sswan55@kaist.ac.kr
Submit the..
  Paper up to 3 pages.
    Include the principle of the mapgen and mcl(roughly).
    Include the explanation of the code you wrote.
    Do not include the ‘Background’. It already lectured by me..
  Video
    Mapgen
    MCL
  Source code

## Slide 6: Tip : Codebook
Opencv
  IMAGE READ : cv::Mat gs = cv::imread(filename, CV_LOAD_IMAGE_GRAYSCALE);
  PIXEL ACCESS : char value = img_map.at<char>(y,x); ( cv::mat img_map)
  IMAGE SHOW : cv::imshow(“window name”,img_map); ( cv::mat img_map)
  https://docs.opencv.org/2.4/modules/core/doc/drawing_functions.html
  Coordinate of image is different from normal coordinate !
  And other useful things.. Like Gaussian blur

## Slide 7: Tip : ROS
ROS
  Refer to LAB#1
  This lab assume that you already install ROS in your desktop.
  http://wiki.ros.org/ROS/Tutorials/WritingPublisherSubscriber%28c%2B%2B%29 (Publisher Subscriber tutorial)
  Useful IDE
    https://ros-industrial.github.io/ros_qtc_plugin/ (qt creator ros)
    http://wiki.ros.org/IDEs